## Slide 1: Basics of Digital Electronics

## Slide 2: Digital Signals
An electrical signal with two discrete levels (high and low)
Two discrete levels are represented by binary digits 0 and 1
referred as Binary number system.
Gorge Boole introduced binary number system with algebra
developed “Boolean Algebra”
Represented in two different ways
  Positive logic system
Negative logic system

## Slide 3: Logic Gates
Basic logic gates
  AND gate
    Logical Multiplication
    Two input gate shown

## Slide 4
Basic logic gates
  OR gate
    Logical Addition
    Two input gate shown
NOT/Inversion gate
  Logical inversion
  Single input single output gate

## Slide 5
Universal logic gates
  NAND gate
    Two input gate shown
NOR gate
  Two input gate shown

## Slide 6
Special gates
  Ex-OR gate
    Two input gate shown
Ex-NOR gate
  Two input gate shown

## Slide 7: Boolean Algebra
Mathematician George Boole developed
rules for manipulation of binary variables.
Rules :
  A+0=A
  A+1=1
  A+A=A
  A+A’=1
  A.0=0
  A.1=A
  A.A=A
  A.A’=0
  A.(B+C)=AB+AC

## Slide 8: Boolean Algebra
A+BC=(A+B).(A+C)
A+A.B=A
A.(A+B)=A
A+A’.B=A+B
A.(A’+B)=A.B
A.B+A’.B’=A
(A+B).(A+B’)=A
A.B+A.C’=(A+C).(A’+B)
(A+B).(A’+C)=AC+A’B
AB+A’C+BC=AB+A’C
(A+B).(A’+C).(B+C)=(A+B).(A’+C)

## Slide 9: De Morgan’s Theorem
(A.B)’=A’+B’
(A+B)’=A’.B’

## Slide 10: Number System
Number System | Base or radix | Symbols used (di or d-f) | Weight assigned to position |  | Example
 |  |  | i | -f | 
Binary | 2 | 0,1 | 2i | 2-f | 10101.10
Octal | 8 | 0,1,2,3,4,5,6,7 | 8i | 8-f | 3547.25
Decimal | 10 | 0,1,2,3,4,5,6,7 ,8,9 | 10i | 10-f | 974.27
Hexadecimal | 16 | 0,1,2,3,4,5,6,7 ,8,9,A,B,C,D, E,F | 16i | 16-f | FA9.46

## Slide 11: Quantities/Counting
Decimal | Binary | Octal | Hexadecimal
0 | 0000 | 00 | 0
1 | 0001 | 01 | 1
2 | 0010 | 02 | 2
3 | 0011 | 03 | 3
4 | 0100 | 04 | 4
5 | 0101 | 05 | 5
6 | 0110 | 06 | 6
7 | 0111 | 07 | 7
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
16 | 1111 | 17 | F

## Slide 12: Number System conversion
Binary to decimal
  Multiply each bit by 2n, n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results Example (110101)2 = ( )10
= 1x25+1x24+0x23+1x22+0x21+1x20
= 32+16+0+4+0+1
= (53)10

## Slide 13: Number System conversion
Binary to octal
  Group bits in threes, starting on right
  Convert to octal number
Example
(110101)2 = ( )8
= 110 101
= 6 5
= (65)8

## Slide 14: Number System conversion
Binary to hexadecimal
  Group bits in fours, starting on right
  Convert to hexadecimal number
Example
(110101)2 = ( )16
= 11 0101
= 0011 0101
= (35)16

## Slide 15: Number System conversion
Decimal to binary
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1Group bits in fours, starting on right
Example
(53)10 = ( )2
= (110101)2

## Slide 16: Number System conversion
Decimal to octal
  Divide by eight, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1Group bits in fours, starting on right
Example
(53)10 = ( )8
= (65)8

## Slide 17: Number System conversion
Decimal to hexadecimal
  Divide by 16, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1Group bits in fours, starting on right
Example (53)10 = ( )16
=
= (35)16 `

## Slide 18: Number System conversion
Octal to binary
  Convert each octal digit to a 3-bit equivalent binary representation
Example
(65)8 = ( )2
= 110 101
= (110101)2

## Slide 19: Number System conversion
Octal to decimal
  Multiply each bit by 8n, n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Example
(65)8 = ( )10
= 6x81+5x80
= 48+5
= (53)10

## Slide 20: Number System conversion
Octal to hexadecimal
  Use binary as an intermediary.
Example
(65)8 = ( )16
= 110 101
= 11 0101
= 0011 0101
= (35)16

## Slide 21: Number System conversion
Hexadecimal to binary
  Convert each hexadecimal digit to a 4-bit equivalent binary representation.
Example
(6A)16 = ( )2
= 0110 1010
= (1101010)2

## Slide 22: Number System conversion
Hexadecimal to octal
  Use binary as an intermediary.
Example
(6A)16 = ( )8
= 0110 1010
= 1 101 010
= 001 101 010
= (152)8

## Slide 23: Number System conversion
Hexadecimal to decimal
  Multiply each bit by 8n, n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results
Example
(6A)16 = ( )10
= 6x161+Ax160
= 6x161+10x160
= 96 + 10
= (106)10

## Slide 24: Complement representation
One’s complement format
  In binary number system, each bit is complimented.
Example
(0100101)2 = (1011010) one’s complement form
Two’s complement format
  In binary number system, each bit is complimented and binary 1 is added.
  Used to represent negative number.
Example
(0100101)2 = (90)10
= (1011010)2 one’s complement form
= (1011010 + 1)2
= (1011011)2 = (-90)10 2’s complement